## Slide 1: SOGRO in Space
Gungwon Kang (KISTI)
On behalf of Y.-B. Bae, W. Kim, C. Park, E. J. Son, J.J. Oh & S.H. Oh (NIMS)
우주 기반 기초과학 워크숍(2020/12/04, 온라인)

## Slide 2: Background
SOGRO (Superconducting Omni-directional Gravitational Radiation Observatory):
  1979: Wagoner, Will & Paik  2016: Paik et al, “Low-frequency terrestrial tensor gravitational-wave detector,” CQG
  2017: KKN 3개 출연연 SOGRO 선행연구 수행
  국내(~15명) 및 U. of Maryland group (~5명): 개념연구 및 Science target 연구 수행 중
  초전도체 활용, 지상기반, 중 주파수대(0.1~10 Hz), 다채널 전방향 텐서 중력파 검출기
(30 m, 50 m, 100 m)
2 m, 1 ton
SOGRO/aSOGRO
pSOGRO
(100~250) tons
≤ 4 K
지하 ~200 m
Moody, Paik, & Caravan (2002)

## Slide 3
(arXiv:1604.00439)
Seismic+Newtonian noises
Due to underground: (200~500) m
Newtonian noise cancellations using seismometers, microphones & tensor channels (Harms & Paik ’15)

## Slide 4: SOGRO in Space

## Slide 5
장점(PROS):
  - Free from Seismic+Newtonian noises
  No need to be underground
  No need to mitigate Newtonian noises
  Cooling down to 50 K by using sunshield layers alone
www.jwst.nasa.gov
Shield size:
MIRI: 7 K using He ref. or cryocooler
L2: ~1.5 million km
Mass: ~705 kg
JWST
SPHEREx
https://spherex.caltech.edu/
Sunshield only: 망원경 전체(), 디텍터)
태양동기화 궤도
Payload Mass: 74.5 kg

## Slide 6
단점(CONS):
  Heavy mass: 100~250 tons, mainly due to platform, cryogenics & test masses
  Cooling ≤ 50 K: He dilution refrigerator
SOLUTIONS:
  ISS 제원: L: 73m W: 109m, M: 419,725kg ~420톤. 1998년 1회 19톤 운송
  Use a single arm: tons. pSOGRO only: 1 or 2 m, ton, single arm ( ton)
  Keep the platform at 50 K  Less sensitivity of ~20 times larger noise strain: Still have science targets!
  Use DECIGO for optical locking to replace the mechanical platform (?)

## Slide 7
Sensitivity for :
,
w/ ,
Less sensitivity, but still have good science targets!

## Slide 8
- Optical locking: Mechanical platform  Optical rigid body
(그림 출처: 김재완 ‘17)
Test Mass
Test Mass
Actuator
Polarizer
Laser
Photodetector
Servo
김재완: “To monitor and control the distance between two test masses with (~1 km arm) precision makes no sense as it would require another LIGO ……”

## Slide 9
(그림 출처: M. Ando ‘14)
-
Sensitivity:
 order of 4 better
But, same frequency bandwidth  Simply a redundant detector?
Any way to make the bandwidths different?

## Slide 10
그림 출처: M. Ando (’14)
,
Need to optimize the design parameters to shift the sensitive bandwidth of SOGRO.
The shot noise of DECIGO increases as .  Optical locking becomes bad.
Should find out some clever way to avoid this dilemma of using optical locking.
More investigation is required.
sSOGRO

## Slide 11
Gravity Gradiometer
SOGRO can be used to measure gravity gradients as well by measuring the common acceleration of test masses.
Ex) SGG (Superconducting GG): Griggs, … Paik ’17 in
  Measure gravity fields of Earth or Moon and draw their gravity maps!
GOCE (Gravity Field and Steady-State Ocean Circulation Explorer)
, ~250 km
GRACE (Gravity Recovery and Climate Experiment)
그림 출처: Ampuero ‘18
pSOGRO
SGG

## Slide 12
결론
“지상기반 소그로  우주기반 소그로”의 장단점을 살펴보고 그 가능성을 모색해 봄
“단축 소형 소그로”를 중력구배계(Gravity Gradiometry)로 활용한 저궤도 지구, 달 탐사 연구
“소그로”: 독창적 원리, 국내 제안, 미답지의 과학적 성과 담보

## Slide 13: 감사합니다!

## Slide 14
예산
Lots of uncertainties, but one may get some hints based on
  2m Prototype SOGRO: ~370억원/6년
  지상 기반 50m SOGRO: (1000~3000)억원/10년
Space SOGRO: ……??